## Slide 1
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Computer System Engineering
IoT-Based Digital Twin for Fault Analysis
& Predictive Maintenance of a DC Motor
Final Year Project Presentation | 2025–26
👤 Students
Abdullah | Ubaid Ullah
🎓 Supervisor
Dr. Qaiser Ajaz
📅 Year
2025 – 2026

## Slide 2
Outline
01
Introduction & Digital Twin Concept
02
Problem Statement & Objectives
03
System Architecture & Hardware
04
ESP32 Firmware & MQTT Communication
05
Dashboard & Digital Twin Visualisation
06
Results, Conclusion & Future Work

## Slide 3
Introduction — Digital Twins & DC Motors
WHAT IS A DIGITAL TWIN?
A Digital Twin is a virtual real-time replica of a physical system that mirrors its behaviour, performance, and health.
Key Capabilities:
Real-time monitoring via IoT sensors
Predictive analytics before failure occurs
Remote diagnostics from anywhere
Reduce unplanned downtime
Why DC Motors?
Used in industry, robotics & automation
Prone to: overheating, overcurrent, vibration, RPM faults
DIGITAL TWIN USE CASES
Improve product quality
74%
Reduce mfg. costs
60%
Increase up-time
38%
Lower maintenance costs
34%
Predictive maintenance
55%

## Slide 4
Problem Statement
Traditional DC motor monitoring systems are reactive — faults are detected only after failure occurs.
This leads to unplanned downtime, high repair costs, and reduced motor lifespan.
🔥
No Real-Time
Fault Detection
Faults like overheating or overcurrent go undetected until motor fails completely.
📡
No Remote
Monitoring
No cloud connectivity — engineer must be physically present to check motor status.
❌
No Predictive
Maintenance
Maintenance is scheduled arbitrarily — no data-driven estimation of remaining life.
Our Solution: IoT-Based Digital Twin with ESP32 + MQTT + Dashboard

## Slide 5
Project Objectives
01
Real-Time Sensing
Read Temp, Current, RPM & Vibration every 500ms using DS18B20, ACS712, Hall sensor & SW-420.
02
On-Board Fault Detection
ESP32 computes fault flags: overheat, overcurrent, vibration persist, RPM drop — all on-device.
03
MQTT Cloud Communication
Publish JSON data to broker.hivemq.com every 500ms. Works on any network — no IP config needed.
04
Digital Twin Dashboard
Python FastAPI dashboard with live Plotly graphs, health status, fault flags & 3D motor model.
05
RUL Estimation in Days
Linear regression on 60s of data estimates Remaining Useful Life for Temp, Current & Vibration.
06
Local Indicators
SH1106 OLED shows live data. RGB LEDs for temperature, current & vibration status on-site.

## Slide 6
System Architecture
SENSORS
DS18B20
Temp GPIO4
ACS712-20A
Current GPIO34
SW-420
Vibration GPIO27
Hall/IR
RPM GPIO14
►
ESP32
• WiFiManager
• Moving Avg Filter
• RPM Interrupt
• Fault Detection
• Health Status
• Circular Buffer (200)
• JSON Builder
• MQTT Publish
MQTT
►
☁ HiveMQ Cloud
broker.hivemq.com
Port: 1883
Topic: motordignostic
►
Dashboard
FastAPI
paho-mqtt
Plotly+3D
▼
OLED
SH1106
RGB
LEDs
Relay
GPIO26

## Slide 7
Hardware Components
Component | Model / Spec | GPIO Pin
Microcontroller | ESP32 (Dual-core 240MHz) | —
Temperature Sensor | DS18B20 (1-Wire) | GPIO 4
Current Sensor | ACS712-20A (100mV/A) | GPIO 34 (ADC)
Vibration Sensor | SW-420 Digital | GPIO 27
RPM Sensor | Hall Effect / IR (1 pulse/rev) | GPIO 14
Relay Module | Active LOW 5V relay | GPIO 26
Push Button | INPUT_PULLUP toggle | GPIO 33
OLED Display | SH1106 128×64 I2C | SDA=21, SCL=22
DC Motor | 12V DC, 3500 RPM no-load | —
RGB LED (Temp) | Red=GPIO15, Green=GPIO2, Blue=GPIO13 | GPIO 15/2/13
Current LEDs | Green=GPIO25, Red=GPIO12 | GPIO 25/12
Vibration LEDs | Green=GPIO5, Red=GPIO32 | GPIO 5/32

## Slide 8
ESP32 Firmware — Key Features
📊 Sensor Reading
• DS18B20 temp every 500ms
• ACS712: 10-sample moving avg
• RPM interrupt + 200µs debounce
• SW-420 vibration digital read
🔍 On-Board Diagnostics
• Temp rate of change (°C/min)
• RPM rate (RPM/min)
• Vibration persistence counter
• Health: OK / Warning / Critical
📡 MQTT Communication
• Broker: broker.hivemq.com:1883
• Topic: motordignostic
• JSON payload every 500ms
• Unique Client ID via chip MAC
💾 Offline Buffering
• Circular buffer: 200 entries
• Stores data on disconnect
• Auto-retransmits on reconnect
• Non-blocking millis() timers

## Slide 9
Fault Detection Logic & Health Status
FAULT FLAGS (4 Types)
🔥
Overheat
Temp > 70°C OR Rate > 2°C/min
⚡
Overcurrent
Current > 15.0 A
📳
Vib Persist
Vibration HIGH for 3+ readings
🔄
RPM Drop
RPM rate < -200 RPM/min
HEALTH STATUS
✅ OK
No faults active. All parameters within normal range.
⚠️ WARNING
Temp>40°C OR RPM<2975 OR Vibration count = 2.
🚨 CRITICAL
Any one or more fault flags are active.

## Slide 10
MQTT Communication — JSON Payload
JSON PAYLOAD (published every 500ms)
{
"timestamp": 123456,
"temperature": 42.5,
"current": 2.30,
"rpm": 3200,
"vibration": 0,
"health": "Warning",
"temp_rate": 1.2,
"rpm_rate": -85.5,
"fault_flags": {
"overheat": 0,
"overcurrent": 0,
"vibration_persist": 0,
"rpm_drop": 1
}
}
MQTT CONFIGURATION
🌐 Broker:
broker.hivemq.com
🔌 Port:
1883 (no auth)
📌 Topic:
motordignostic
📶 QoS:
QoS 0, No Retain
⏱ Interval:
Every 500ms
🔑 Client ID:
ESP32_MAC (unique)
☁ Network:
Any WiFi / Hotspot
🔄 Reconnect:
Auto every 5 seconds

## Slide 11
Python Dashboard — Overview
📈
4 Live Plotly Graphs
Temp, Current, RPM, Vibration — 200-point rolling window, 500ms updates
🎚️
Alert Threshold Sliders
3 adjustable sliders: Vib (1-10g), Temp (40-100°C), Current (1-15A)
⏳
RUL Estimation in Days
Linear regression on last 60s of data → Remaining Useful Life per parameter
⚠️
4 Fault Flag Cards
Real-time Overheat, Overcurrent, Vib Persist, RPM Drop status indicators
🔩
Interactive 3D Motor
Three.js cylinder model with OrbitControls — drag to rotate, scroll to zoom
📥
CSV Export Button
One-click download of all graph data as timestamped CSV file
Tech Stack: FastAPI | paho-mqtt | Plotly.js | Three.js | WebSocket | Uvicorn

## Slide 12
Remaining Useful Life (RUL) Estimation
Method: Linear Regression on last 60 seconds (120 samples) of sensor data
RUL (days) = (Critical Threshold – Current Value) ÷ Slope × 0.5 sec ÷ 86400
🌡️ Temperature
Critical: 95°C
Current: ~42°C
Linear slope from 60s window
>7d
1-7d
<1d
⚡ Current
Critical: 6.0 A
Current: ~2.3A
Trend from 120 data samples
>7d
1-7d
<1d
📳 Vibration
Critical: 1 (persist)
Current: 0
Counts persistent HIGH reads
>7d
1-7d
<1d

## Slide 13
Results & System Performance
⏱
500 ms
Sampling & Publishing Rate (2Hz real-time)
📡
<200ms
MQTT Latency (typical on WiFi)
💾
200 pts
Circular Buffer Offline Capacity
🔋
~180mA
ESP32 Typical Current Draw
KEY ACHIEVEMENTS
✅ Successful fault detection for all 4 fault types (Overheat, Overcurrent, Vib Persist, RPM Drop)
✅ RUL estimation functional using linear extrapolation — output in days with 3 colour zones
✅ Dashboard operational on any network via HiveMQ public broker — zero IP configuration
✅ OLED + RGB LEDs providing accurate real-time local feedback on all sensor states
✅ Circular buffer ensures zero data loss during MQTT disconnection — auto-retransmits on reconnect

## Slide 14
Our System vs Traditional Monitoring
Feature | Traditional System | Our IoT System
Monitoring Approach | ❌ Manual / periodic | ✅ Real-time every 500ms
Fault Detection | ❌ After failure only | ✅ Predictive — before failure
Remote Access | ❌ None | ✅ Cloud via HiveMQ MQTT
Network Dependency | ❌ Fixed IP required | ✅ Any WiFi / hotspot
Data Logging | ❌ Paper or local only | ✅ Cloud + CSV export
RUL Estimation | ❌ None | ✅ Days estimate (3 parameters)
Local Feedback | ❌ None | ✅ OLED + RGB LEDs
Cost | ❌ Expensive hardware | ✅ Low-cost IoT components

## Slide 15
Challenges & Future Work
CHALLENGES FACED & SOLUTIONS
⚡ ACS712 ADC Noise
→ Implemented 10-sample moving average filter for stable current readings.
⚡ RPM Interrupt Bounce
→ Added 200µs micros() debounce in ISR to eliminate false pulse counts.
⚡ MQTT IP Dependency
→ Switched to public HiveMQ broker — works on any network without IP config.
⚡ Client ID Collision
→ Generated unique Client ID using ESP32 chip MAC address.
⚡ WiFi Credential Entry
→ Integrated WiFiManager — captive portal on first boot, no hardcoding.
FUTURE WORK
🤖 ML Fault Classification
Train ML model to auto-classify fault type from sensor patterns.
📱 Mobile App
Flutter/React Native app for real-time motor monitoring on phone.
🔄 AC Motor Extension
Extend system to 3-phase AC induction motors.
🛜 OTA Firmware Updates
Add Over-The-Air firmware upgrade capability.
📊 More Parameters
Add back-EMF, power factor, bearing temperature sensors.

## Slide 16
Conclusion
🎯
Complete IoT Digital Twin built for real-time DC motor fault analysis & predictive maintenance
⚙️
ESP32 performs edge diagnostics + publishes JSON via MQTT to HiveMQ cloud every 500ms
📊
Python dashboard: 4 live graphs, RUL in days, fault flags, 3D motor model & CSV export
☁️
System is location-independent — works on any WiFi or hotspot via public MQTT broker
🔮
Scalable architecture — extensible to other industrial motors & IoT predictive maintenance
15 Slides Presentation
9 Sensors & Outputs
4 Fault Types
200 Buffer Points

## Slide 17
References
[1] M. Grieves, "Digital Twin: Manufacturing Excellence through Virtual Factory Replication," White Paper, 2014.
[2] F. Tao et al., "Digital Twin-Driven Product Design, Manufacturing and Service," Int. J. Adv. Manuf. Technol., 2018.
[3] A. Rassõlkin et al., "Digital twin of an electrical motor based on empirical performance model," IEEE ICEPDS, 2020.
[4] T. D. Lopes et al., "The Use of Digital Twins in Finite Element for Induction Motors Faults," Sensors, 2021.
[5] Espressif Systems, "ESP32 Technical Reference Manual," espressif.com, 2023.
[6] HiveMQ, "MQTT Essentials — A Complete Guide to MQTT," hivemq.com, 2023.
[7] Eclipse Foundation, "Paho MQTT Python Client Documentation," eclipse.org.
[8] Plotly Technologies, "Plotly Python Open Source Graphing Library," plotly.com.

## Slide 18
Thank You
Any Questions?
IoT-Based Digital Twin for Fault Analysis & Predictive Maintenance of a DC Motor
👤 Abdullah | Ubaid Ullah
🎓 Supervisor: Dr. Qaiser Ajaz | Academic Year: 2025–26
Dept. of Computer System Engineering — The Islamia University of Bahawalpur